CutDownRemote
Lou Nigra
Adler Planetarium – Far Horizons
Rachael Affenit
Illinois Institute of Technology
Kelli W.

Summary:
The CutDownRemote will receive information and new code via Xbee from the CutDownBase. Timer and all other variables can be set remotely via CutDownBase.

The CutDownRemote contains a timer, which can also be changed via the button interface.

When the CutDownRemote capacitors are fully charged (~4.5 volts), charging will cease until charge level has dropped a designated percent below the target value, then resume.

Indicators:
- LED (Charge)
  - Off >> Not yet charged
  - On >> Fully charged
- LED (Timer)
  - Off >> Timer inactive
  - Flashing every 1 second >> Timer active and counting down
- LED (Set Mode)
  - Off >> Not in “Set” Mode
  - On >> Inside “Set” Mode (hold down “Set” switch to deactivate)
- Row of LEDs (Current Variable on Display Lit)
  - Time >> “Timer” LED Lit
  - % Charge on Battery >> “Batt” LED Lit
  - % Charge on Capacitors >> “Cap” LED Lit

Controls:
- Start/Stop Toggle Switch (Timer)
  - Start Timer: Push in switch
  - Stop Timer: Push in and release switch
    - Timer LED turns off
- Set Toggle Switch
  - Enter Set Mode: Push in switch
  - Done Setting Time: Push in and release switch
- Up/Down Momentary Contact Switches (Change time in Set mode)
  - Press up/down buttons to set time
  - Buttons change time by 1 minute in each direction
- Change Variable Momentary Contact Switch
  - Scroll through variables values on display: Press switch (reacts on touch)